## Slide 1
1
School of Electronics Engineering (SENSE)
Project-I (2026)
Design of a Temperature-Compensated PLL Frequency Synthesiser
Student Name(s):
Aaryan Dogra (23BEC1032) · Yugeshwaran (23BEC1404) · Viju Sanjai (23BEC1306)
Guide:
Dr. B. Bindu, School of Electronics Engineering (SENSE)
Programme / School:
B.Tech — SENSE, VIT Chennai
Review & Date:
Final Review (Review-III) · 28.10.2026
Guide's Signature with Date
Signature: _____________________
Date: _________________________

## Slide 2
2
Problem & Objectives
Problem
A ring-VCO drifts with temperature: threshold voltage, mobility and capacitance all shift, so the same control voltage gives a different frequency hot vs cold. Process corners change the size of the drift.
Objectives
Integer-N charge-pump PLL in sky130B, open-source and headless (ngspice 47): REF 28.275 MHz -> PFD -> charge pump -> loop filter -> 5-stage current-starved ring VCO -> /8.
Measure the uncompensated drift on every process corner, design a temperature-compensation, and validate it with Monte Carlo and hypothesis tests.
Close the loop and check lock time across corners and temperature.
226.2 MHz
target at V_ctrl = 0.9 V (tt, 27 C) = 8 x 28.275 MHz
+/-0.3 %
frequency-drift target over -40 to 85 C
< 2 us
lock-time target
Takeaway: we need a drift figure measured on the real topology and process, then a correction that is proven, not assumed.

## Slide 3
3
Detailed Literature Review
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
1 | G. Souliotis et al., 2022 | Temperature compensated ring oscillator based VCO, AEU Int. J. Electron. Commun. | PTAT current compensation of a ring VCO inside a PLL; 180nm, 480MHz, fabricated | Closest topology benchmark: -1.5%/+0.4% over -40->120C, measured. First-order only; different node
2 | C. Stancu et al., 2023 | Temp. and power-supply compensated CMOS clock circuit based on ring osc., Electronics | Temp + supply compensated 50MHz ring-oscillator clock; simulation only | 1.6% temperature error pre-layout. A clock circuit, never closed into a PLL
3 | Z. Geng et al., 2018 | Low power fast locking PLL freq. synthesizer with temp. compensation, EAME | Freq. presetting + dynamic loop BW + static/dynamic temp. comp.; 180nm, 2.1-2.6GHz | Lock <2us over 0-80C, -117dBc/Hz@1MHz, 9mW. Stability claim is the locked output, set by the crystal
4 | Y. You et al., 2014 | 12GHz 67% tuning, 0.37ps RJrms PLL, LC-VCO temp. comp., 0.13um CMOS, IEEE RFIC | LC-VCO PLL for serial links; comp. scheme preserves tuning range; 5.6-13.4GHz | Stays locked -40->85C. Needs inductor models our process supports poorly; not portable to a ring VCO
5 | S. Sinha, 2002 | Design of an integrated CMOS PLL frequency synthesizer, IEEE MELECON | Dual-loop CP-PLL, 0.35um, 2.4-2.5GHz, 1MHz steps | -82dBc/Hz@10kHz. Architectural reference for our loop; no temperature compensation
6 | E. M. V. Freitas et al., 2025 | Using open source EDA tools in ASICs for HEP: a mixed comparison, JINST | Open-source vs commercial flows on IHP 130nm blocks incl. a current-starved ring VCO | Digital QoR quantified (+53% area, +118% power); analog VCO comparison qualitative, open-loop, no MC
7 | M. Thiriloganathan et al., 2026 | 2.4GHz LC-VCO fractional-N PLL, open-source, 130nm BiCMOS, SMACD | Fully open-source flow (Xschem/ngspice/KLayout/OpenEMS), EM-modelled inductor | -100.8dBc/Hz@1MHz. Closes a loop open-source, but no temp. compensation, no PVT/Monte Carlo
8 | R. N. S. Raphael et al., 2019 | PLL-based frequency synthesizer for digital systems driving, BTSym'18 (Springer) | 3rd-order CP-PLL for clock generation, integer-N (N=8-16), VCO input-cap-aware LF model | Settling <2us. Same loop class as ours; no temperature compensation

## Slide 4
4
Detailed Literature Review (contd.)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
9 | Y. Li, K. Du, J. Zhang, 2022 | Design of ring oscillator with temperature compensation effect, Int. J. RF Microw. CAE | Positive-TC supply voltage on a 31-stage ring, 0.18um; 33kHz sleep timer | 120 ppm/C (1.6%) over -40->80C. Single linear coefficient; kHz timer, not a PLL
10 | H. H. Hammam et al., 2022 | An ultra-low-power process-and-temperature compensated ring oscillator, IEEE ICEEE | 3-stage current-starved ring, 130nm, process + temperature compensation | Up to 90% less variation vs. plain current-starved ring, 346nW. Standalone oscillator
11 | S. Zhang et al., 2016 | Temperature compensation technique for ring oscillators with tail current, Electron. Lett. | Tail current = constant source + PTAT current, first-order | Foundational first-order technique; no numbers reported in abstract; not closed-loop
12 | M. Ortner, M. Punzenberger, 2017 | Oscillators using quadratic temperature compensation, US Pat. 9,748,962 B2 | Linear + quadratic temperature term for a VCO, -40->85C | Generic 2nd-order compensation is patented -- narrows our claim to ring-VCO + closed PLL + open PDK + stats
13 | D. Patrinos, G. Souliotis, 2025 | Low-voltage, low-power 2.5GHz ring oscillator with process & temp. comp., JLPEA | PTAT current + process-corner detection/tuning; 22nm, 0.8V; post-layout sim | Drift 23.9%->5.4% (tt) and 47.3%->7.2% (PVT). Corner-aware like our C(corner); not in a PLL
14 | M. Sivasakthi, P. Radhika, 2024 | PVT tolerant hybrid current starved ring VCO, bulk-driven keeper, 45nm, AEU | Two current-starved ring VCOs; Cadence GPDK45; corner + Monte Carlo | 6.97GHz, -121.5dBc/Hz@1MHz. PVT tolerance of the VCO itself, no compensation network or loop
15 | S. Madheswaran, R. Panneerselvam, 2024 | 7-stage MCML power-gated current starved VCO for PLL, IJECE | MOS current-mode logic delay cells with power gating, 45nm, simulation | 3.06GHz, -125.9dBc/Hz. Same device class as ours; no closed-loop temperature characterisation
Research gap (from all 15): no reported work combines a compensated ring VCO inside a closed loop, characterised across process corners with Monte Carlo rigor -- that gap is what this project fills.

## Slide 5
5
Novelty, Patent and Research Gap
What is NOT novel
Generic quadratic (2nd-order) temperature compensation of an oscillator is patented: US 9,748,962 B2 (Ortner and Punzenberger, Infineon, 2017) [12]. We do not claim it.
Current-starved ring VCOs and the charge-pump PLL topology are textbook.
What this project adds
A closed-loop, per-corner, statistically validated study of a compensated ring-VCO PLL on an open PDK (sky130B), with the failures and corrections documented.
Research gap (from 15 IEEE-level references)
No reported work combines a compensated ring VCO inside a closed loop, characterised across process corners with Monte Carlo rigour.
15 refs
read; closest: Souliotis 2022 [1], Stancu 2023 [2], Geng 2018 [3]
1 patent
narrowed the claim to ring-VCO + closed PLL + open PDK + statistics
Open PDK
everything reproducible: ngspice + sky130B, no licensed tools yet
Takeaway: our contribution is the validated closed-loop study, not the idea of 2nd-order compensation.

## Slide 6
6
Methodology: Review 1 -> Review 2 -> Review 3
Takeaway: characterise, compensate, close the loop, then validate statistically.

## Slide 7
7
System Architecture
20 uA
charge pump (behavioural), 5x until first divider edge
3.6 kOhm
R2 (retuned from 1.7 k); C1 68 pF, C2 6.8 pF
5 stages
current-starved ring VCO, tunes 18 -> 358 MHz
/ 8
divider (3 T flip-flops)
Takeaway: a standard integer-N loop, so every difference we see comes from the VCO and its compensation.

## Slide 8
8
VCO: Schematic & Tuning Curve
Chart: Control voltage V_ctrl (V)
| 0.65 | 0.7 | 0.8 | 0.9 | 0.95 | 1.1 | 1.25 | 1.4
sf | 34.3768 | 68.5981 | 165.0304 | 246.1908 | 269.1682 | 300.2874 | 313.7819 | 321.5885
ff | 29.8597 | 63.4213 | 168.0956 | 279.1783 | 320.4279 | 380.1118 | 403.8636 | 417.1975
tt | 17.9752 | 41.2937 | 125.171 | 226.2061 | 266.06 | 324.074 | 345.9747 | 358.0532
ss | 10.4693 | 25.7261 | 89.5449 | 177.9927 | 215.3445 | 270.1737 | 289.6513 | 300.1703
fs | 8.4031 | 21.9705 | 84.9899 | 183.6596 | 233.7548 | 328.2707 | 362.2761 | 379.8137
~890 MHz/V
local K_VCO at 0.9 V (tt)
18 -> 358 MHz
over 0.65 -> 1.40 V (tt)
Takeaway: V_ctrl sets the starving current; 0.9 V gives the 226 MHz target. K_VCO is ~890 MHz/V (an earlier 669 was wrong).

## Slide 9
9
Uncompensated Drift: PDK Corners
Chart: Temperature (C)
| -40 | -20 | 0 | 27 | 50 | 85
sf (112 ppm/C) | -1.3317 | -0.79546 | -0.37811 | 0 | 0.15299 | 0.070891
ff (332 ppm/C) | -3.261 | -1.9897 | -0.98398 | 0 | 0.53761 | 0.88965
tt (681 ppm/C) | -6.0433 | -3.7977 | -1.9502 | 0 | 1.2348 | 2.4664
ss (1070 ppm/C) | -9.208 | -5.8462 | -3.0375 | 0 | 1.9985 | 4.1638
fs (1399 ppm/C) | -11.8985 | -7.5912 | -3.9608 | 0 | 2.6448 | 5.5886
+/-0.3 % spec | 0.3 | 0.3
 | -0.3 | -0.3
12.5x
tempco spread, sf 112 to fs 1399 ppm/C
8.51 %
tt frequency span, -40 to 85 C
112 - 1399
ppm/C across the 5 PDK corners
Takeaway: every corner is far outside +/-0.3 % without compensation, and the corners disagree by a factor of 12.

## Slide 10
10
Why the Corner Numbers Looked Out of Range
In review, ff / tt / fs / sf values were not in the ranges they are meant to be. We audited it (ngspice 47, same PDK).
Verdict: the simulations were fine. Three things were wrong in how we expected and described the corners.
1. Labels
In this PDK sf = fast-NMOS / slow-PMOS and fs = slow-NMOS / fast-PMOS (measured). Earlier labels were reversed.
2. Expectation
'Skew corners lie between ss and ff' is false in sky130: its skew corners shift each device further than ss/ff do. At the VCO's low bias this is amplified to about 9 %.
3. Tempco is not bounded by ff and ss
Even in a clean textbook NMOS x PMOS set the tempco extremes sit at the skew corners.
Takeaway: nothing was broken; our expectation of the corner envelope was wrong.

## Slide 11
11
Audit 1: PDK Skew Corners Are Wider Than ss / ff
Threshold shift vs tt (mV) | ss | ff | PDK sf | PDK fs
NMOS Vth | +25 | -25 | -36 | +36
PMOS ¦Vth¦ | +15 | -23 | +32 | -43
The extracted device thresholds of the skew corners move further than ss/ff.
At the VCO bias (0.9 V, overdrive only ~0.2 V) an extra ~11 mV of Vth is ~9 % of drive current.
At 1.8 V the same corners agree within 1 %.
~9 %
skew corners fall outside the ss-ff envelope at 0.9 V
< 1 %
outside the envelope at 1.8 V
11 corners
9 textbook + PDK sf + PDK fs
Takeaway: the PDK defines its skew corners more aggressively than ss/ff, so they can fall outside them.

## Slide 12
12
Audit 2: Device Current vs the ss-ff Envelope
25.3 - 51.3 uA
NMOS Id at 0.9 V: fs 25.3, ss 27.9, tt 36.9, ff 47.7, sf 51.3
397 - 480 uA
NMOS Id at 1.8 V: skews within 1 % of ss/ff
8 - 9 %
skews outside the ss-ff envelope at 0.9 V
Takeaway: at the low VCO bias, skew corners step outside ss/ff; at full gate drive they do not.

## Slide 13
13
Audit 3: A Textbook 3 x 3 Corner Set
8 / 8
ordering checks pass (f rises with N and P strength at 0.9 and 1.4 V; tempco falls with N strength)
178.0 - 279.2 MHz
f at 0.9 V across the 9 textbook corners
306 - 1151
textbook tempco range ppm/C (3.8x) vs PDK 5-corner 112 - 1399 (12.5x)
Takeaway: with N and P varied independently the ordering is textbook-clean; only the PDK skews break the tempco range.

## Slide 14
14
Audit 4: Tempco Follows NMOS Drive
-0.78 / -1.1
Vth tempco mV/C, NMOS / PMOS (textbook -0.5 to -3)
-30 % / +14 %
NMOS Id over 125 C at 1.8 V / 0.9 V
-816 ppm/C
tt tempco at V_ctrl = 1.4 V (sign flips from +681 at 0.9 V)
Takeaway: weaker NMOS drive means larger positive tempco; the bias sits below the zero-tempco point.

## Slide 15
15
Tempco Mechanism and Physics Checks
Why the frequency rises with temperature at 0.9 V
Vth falls with temperature (about -0.8 mV/C NMOS). With only ~0.2 V overdrive, that gain wins over the mobility loss, so drive current rises.
Which device limits the ring depends on V_ctrl
At 0.9 V the NMOS dominates (36 % spread slow to fast N vs 10 % across P). At 1.4 V the PMOS dominates (26 % vs 9 %).
Other checks that pass
Supply current is proportional to f in every corner (C ~ 27-30 fF per node). Closed-loop lock voltage equals the open-loop value for 226.2 MHz within 0.2 mV at all 11 corners.
36 % vs 10 %
0.9 V: NMOS vs PMOS spread
26 % vs 9 %
1.4 V: PMOS vs NMOS spread
0.2 mV
lock V vs open-loop V, 11 corners
Takeaway: the tempco mechanism is overdrive, not N/P balance; every physics check agrees with theory.

## Slide 16
16
Compensation Architecture
dV(T)
correction added to V_ctrl before the VCO bias generator
1st order
k1 (T - 27): PTAT/CTAT equivalent
2nd order
adds k2 (T - 27)^2 for the curvature
Ideal
behavioural source; transistor-level network is future work
Takeaway: the correction is a voltage added to V_ctrl: v_eff = v + k1 (T-27) + k2 (T-27)^2.

## Slide 17
17
Compensation Method: Fit, Then Verify
scripts/comp_factorial.py, applied per corner
1. Measure f(T, V) at V = 0.85 / 0.9 / 0.95 V for 6 temperatures.
2. Solve the exact voltage shift dV*(T) that restores f(27 C).
3. Least-squares fit k1 (1st order) and k1, k2 (2nd order).
4. Verify by simulating the compensated VCO at the 6 fit temperatures and at 4 held-out temperatures (-30, 10, 40, 70 C).
Why Review 2's numbers changed
Review 2 used a wrong K_VCO (669 instead of ~890 MHz/V) and an analytic first-order guess. The measured fit replaces it: tt span 1.12 % -> 0.20 %.
-1.543e-4
k1 at tt (V/C)
4.18e-7
k2 at tt (V/C^2)
4 held-out
temperatures never used in the fit
Takeaway: coefficients come from measured data and are checked at temperatures the fit never saw.

## Slide 18
18
Compensation at the Typical (tt) Corner
8.51 -> 0.20 %
span: baseline -> 2nd order (1st order 0.67 %)
0.16 %
max deviation; +/-0.3 % spec MET
0.09 %
max deviation at held-out temperatures
Takeaway: at tt the compensated VCO stays within +/-0.16 % over -40 to 85 C.

## Slide 19
19
Compensation on 11 Corners
8 / 11
corners meet +/-0.3 % (7 of 9 textbook)
31 - 44x
compensation ratio (PDK sf 15.9x)
0.03 - 0.25 %
held-out max deviation
Takeaway: 8 of 11 corners meet the spec; the slow-NMOS corners are the hardest.

## Slide 20
20
Compensation Results: All 11 Corners
Corner | f 0.9 V (MHz) | Base span % | 1st % | 2nd % | Max dev % | Held-out % | Ratio C | +/-0.3 %
N slow / P slow (ss) | 178.0 | 13.37 | 0.91 | 0.35 | 0.277 | 0.175 | 38.4 | yes
N slow / P typ | 188.0 | 13.97 | 0.98 | 0.38 | 0.301 | 0.201 | 37.2 | NO
N slow / P fast | 195.9 | 14.38 | 1.10 | 0.42 | 0.325 | 0.223 | 34.3 | NO
N typ / P slow | 211.8 | 8.10 | 0.64 | 0.24 | 0.195 | 0.109 | 33.6 | yes
N typ / P typ (tt) | 226.2 | 8.51 | 0.67 | 0.20 | 0.162 | 0.091 | 43.2 | yes
N typ / P fast | 238.1 | 8.79 | 0.77 | 0.20 | 0.168 | 0.097 | 43.7 | yes
N fast / P slow | 242.8 | 3.82 | 0.45 | 0.12 | 0.079 | 0.034 | 31.0 | yes
N fast / P typ | 262.7 | 4.06 | 0.50 | 0.12 | 0.102 | 0.041 | 33.3 | yes
N fast / P fast (ff) | 279.2 | 4.15 | 0.59 | 0.11 | 0.093 | 0.035 | 37.0 | yes
PDK sf (N fast / P slow) | 246.2 | 1.49 | 0.41 | 0.09 | 0.051 | 0.036 | 15.9 | yes
PDK fs (N slow / P fast) | 183.7 | 17.49 | 1.29 | 0.49 | 0.360 | 0.251 | 35.8 | NO
Takeaway: NOT met: N slow / P typ 0.301 (borderline), N slow / P fast 0.325, PDK fs 0.360. Nominal, ideal source.

## Slide 21
21
Monte Carlo (n = 72 chips, tt): Mean |Drift|
Chart: Mean |drift| (MHz), 95 % CI bars
| Baseline 20.11 | 1st order 3.25 | 2nd order 2.76
mean ¦f(85C) - f(-40C)¦ (MHz) | 20.11 | 3.25 | 2.76
-17.35 MHz
baseline -> 2nd order, CI [16.37, 18.34], 72/72 chips
-16.86 MHz
baseline -> 1st order, CI [15.57, 18.16], 71/72 chips
0.49 MHz
1st vs 2nd order: CI [-0.26, 1.24], NOT significant (2nd smaller in 40/72)
Takeaway: compensation cuts drift ~7x (72/72 chips), but the 2nd-order term adds no detectable benefit under mismatch.

## Slide 22
22
Monte Carlo: The Mismatch Floor
~3 MHz
residual drift (~1.2-1.4 % of 226 MHz)
0.2 - 0.7 %
nominal residual without mismatch
Per-chip trim
needed to reach +/-0.3 % across chips (future work)
Takeaway: transistor mismatch makes each chip drift differently, and one global correction cannot remove it.

## Slide 23
23
Loop Dynamics: Found, Fixed, Verified
Found
The Review-1 loop design dropped a 1/(2 pi) factor in omega_n^2, so damping was zeta ~0.33, not the 0.72 claimed. The original loop had not settled at ss/ff/sf/fs within 2 us.
Fixed
R2 retuned 1.7 k -> 3.6 kOhm: zeta ~0.70, phase margin ~65-70 deg (100 x zeta rule, not a Bode plot).
Cost
Cold start is slower (tt 839 -> 1351 ns) but in spec; coarse start faster (577 -> 503 ns).
zeta 0.33 -> 0.70
damping
8.6 -> 0.35 mV
V_ctrl ripple at lock
0.78 -> 0.008 %
final frequency error
Takeaway: we caught a design-equation error ourselves; the retuned loop is well damped and quiet.

## Slide 24
24
Cold-Start Fix: Boosted Charge Pump
Problem
From 0 V the VCO is in deep subthreshold (0.6 MHz at 0.5 V, 6.5 MHz at 0.6 V vs 226 MHz target), so the divider clock is effectively absent and the pump-up is slow.
Fix
Charge pump runs at 5 x I_cp until the divider's first edge, then drops to 20 uA.
1351 ns
tt lock from 0 V
503 ns
tt lock from 0.85 V
Takeaway: the boosted pump removes the dead zone at start-up; lock is inside 2 us.

## Slide 25
25
Cold-Start Traces
1283 - 1675 ns
cold-start lock, 11 corners, 27 C
<= 0.8 mV
V_ctrl ripple in every run
226.17 MHz
= 8 x f_ref (-0.01 %) in every run
Takeaway: from 0 V the control voltage climbs and settles to its corner-specific value.

## Slide 26
26
Lock Time Across 11 Corners (27 C)
Chart: Lock time (ns), spec < 2000
| NsPs | NsPt | NsPf | NtPs | NtPt | NtPf | NfPs | NfPt | NfPf | PDK sf | PDK fs
Coarse start (0.85 V) | 966.8 | 645.3 | 572.8 | 677.5 | 503.1 | 177.4 | 386.9 | 279.1 | 241.1 | 419.3 | 575.5
Cold start (0 V, boosted CP) | 1675 | 1531.2 | 1354.4 | 1537 | 1351.4 | 1318.1 | 1390.8 | 1315.8 | 1282.5 | 1387.8 | 1355.1
177 - 967 ns
coarse start
1283 - 1675 ns
cold start
22 / 22
runs inside 2 us at 27 C
Takeaway: all 11 corners lock inside 2 us at 27 C; slow-NMOS corners take longest. (Ns = N slow, Pf = P fast, etc.)

## Slide 27
27
Does the Loop Lock at the Right Voltage?
< 0.2 mV
lock V vs open-loop V for 226.2 MHz, 11 corners
0.849 - 0.968 V
lock V_ctrl range, ff to ss at 27 C
+11.9 / -7.5 mV
tt lock-V shift at -40 / 85 C = fitted compensation (+12.2 / -7.5)
Takeaway: the PLL absorbs the VCO tempco; at tt this independently confirms the compensation fit.

## Slide 28
28
Temperature: Cold-Start Lock at -40, 27, 85 C
2083 ns
ss at 85 C: MISSES the 2 us spec by 4 %
1319 / 1418 ns
tt at -40 / 85 C
1249 / 1317 ns
ff at -40 / 85 C
Takeaway: worst case ss / 85 C misses the lock spec slightly; every other case is inside it.

## Slide 29
29
Benchmark vs Literature (Honest)
Design | Process / basis | Residual drift | Lock time
This work, 2nd order (tt, nominal) | sky130, simulation, ideal source | +/-0.16 % max dev (0.20 % span), -40 to 85 C | 1351 ns (0 V cold start)
This work, 2nd order (MC n = 72) | sky130, simulation, mismatch on | ~2.76 MHz = ~1.2 % ¦drift¦, 85 vs -40 C | n/a
Souliotis 2022 [1] | 180 nm, measured silicon | -1.5 % / +0.4 %, -40 to 120 C | not reported
Stancu 2023 [2] | simulation, 50 MHz clock | 1.6 % temperature error | n/a
Geng 2018 [3] | 180 nm, measured silicon | not reported as drift | < 2 us
Nominal simulation of an ideal network is competitive, but it is not like-for-like with measured silicon or with a transistor-level circuit. With chip-to-chip mismatch our residual (~1.2 %) is the same order as the published numbers.
No jitter or phase-noise number yet (no PSS/Pnoise in open tools), so [3]'s -117 dBc/Hz cannot be compared.
Takeaway: in the right ballpark, not proof of parity with fabricated designs.

## Slide 30
30
What We Found and Corrected
# | Earlier claim | Corrected
1 | sf / fs labels (sf = slow N) | reversed: PDK sf = fast N / slow P (measured)
2 | Tempco set by N/P balance | set by NMOS overdrive; sign flips at 1.4 V
3 | K_VCO = 669 MHz/V | ~890 MHz/V (887 local slope at 0.9 V)
4 | Hard oscillation floor at 0.63 V | none: 0.63 MHz at 0.5 V, 6.5 MHz at 0.6 V (window artefact)
5 | Loop zeta 0.72 (1/(2 pi) dropped) | zeta 0.33 -> retuned R2 = 3.6 k gives ~0.70
6 | Compensation coefficients (wrong K_VCO) | refit: tt 0.16 % max dev, 8 / 11 corners meet spec
7 | 2nd order significantly better (n = 30) | n = 72, corrected fit: not significant; mismatch floor ~1.2-1.4 %
8 | PDK skew corners lie inside ss-ff | wider than ss/ff; textbook 3 x 3 set added
9 | Closed loop fine in all cases | ss / 85 C cold start 2083 ns misses 2 us by 4 %
Takeaway: each fix came from our own audit and each is traceable to a re-run.

## Slide 31
31
Known Limitations
Compensation network and charge pump are behavioural (ideal) models; no transistor-level versions yet.
No layout, DRC, LVS or post-layout simulation yet.
No jitter or phase-noise number (no PSS/Pnoise in open tools).
Phase margin is the 100 x zeta rule, not a Bode plot.
Only R2 = 1.7 / 3.0 / 3.6 kOhm simulated at transistor level; 3.6 k is not claimed optimal.
Cold start simulated on 11 corners at 27 C and at 3 corners for +/-temperature, not all 11 x all T.
Compensation is fitted nominally at V_ctrl = 0.9 V; each corner actually locks at 0.85 - 0.97 V.
Mismatch limits compensated drift to ~1.2-1.4 %; the H1 test and Spectre arm are pending.
Takeaway: we state plainly what is ideal, nominal, or still missing.

## Slide 32
32
Remaining Work / Next Phase
Circuit
Transistor-level charge pump and compensation network (PTAT/CTAT + squarer), then re-run the loop.
Define the compensation at each corner's own lock voltage; per-chip trim to beat the mismatch floor.
Physical design
Layout in Magic, DRC, LVS (netgen, built), post-layout simulation.
Validation and release
Virtuoso/Spectre cross-check arm, PSS/Pnoise, H1 regression (needs department Virtuoso access - to confirm with Dr. Bindu).
Spec sign-offs (V_ctrl floor revision, +/-0.15 ppm restatement); paper and artifact release.
Takeaway: the behavioural result is solid; the next phase makes it real hardware-shaped.

## Slide 33
33
Final Review at a Glance
8 / 11
corners meet +/-0.3 % (tt 0.16 % max dev)
8.51 -> 0.20 %
tt span, baseline -> 2nd order
31 - 44x
compensation ratio (PDK sf 15.9x)
20.1 -> 2.8 MHz
Monte Carlo |drift|, n = 72
1.2 - 1.4 %
mismatch floor (per-chip trim needed)
177 - 967 ns
coarse-start lock, 11 corners, 27 C
1283 - 1675 ns
cold-start lock, 11 corners, 27 C
2083 ns
ss / 85 C cold start: misses 2 us by 4 %
zeta ~0.70 (R2 = 3.6 k); 15 references; 1 patent narrowed the claim; 9 corrections found by our own audit.
Takeaway: a verified, honest closed-loop study with its limits stated.

## Slide 34
34
References
[1] G. Souliotis, E. Keramida, F. Plessas, R. Malatesta, and S. Vlassis, “Temperature compensated ring oscillator based VCO,” AEU – Int. J. Electron. Commun., vol. 149, Art. no. 154195, May 2022.
[2] C. Stancu, A. Neacsu, O. Profirescu, D. Dobrescu, and L. Dobrescu, “Temperature and power supply compensated CMOS clock circuit based on ring oscillator,” Electronics, vol. 12, no. 3, Art. no. 507, Jan. 2023.
[3] Z. Geng, X. Ma, and Z. Li, “A low power fast locking PLL frequency synthesizer with temperature compensation,” in Proc. 3rd Int. Conf. EAME, Atlantis Press, Jun. 2018, pp. 281–285.
[4] Y. You, D. Huang, J. Chen, and S. Chakraborty, “A 12GHz 67% tuning range 0.37ps RJrms PLL with LC-VCO temperature compensation scheme in 0.13µm CMOS,” in Proc. IEEE RFIC, Tampa, FL, USA, Jun. 2014, pp. 101–104.
[5] S. Sinha, “Design of an integrated CMOS PLL frequency synthesizer,” in Proc. 11th IEEE MELECON, Cairo, Egypt, 2002, pp. 220–224.
[6] É. M. V. Freitas et al., “Using open source EDA tools in ASICs for HEP: A mixed comparison,” J. Instrum., vol. 20, no. 12, Art. no. P12022, Dec. 2025.
[7] M. Thiriloganathan et al., “A 2.4 GHz LC-VCO fractional-N phase locked loop open-source design in 130-nm BiCMOS,” in Proc. 22nd Int. Conf. SMACD, 2026, arXiv:2607.08852.
[8] R. N. S. Raphael, A. M. Pinto, L. T. Manera, and S. Finco, “Phase-locked loop (PLL)-based frequency synthesizer for digital systems driving,” in Proc. BTSym’18, SIST vol. 140, Springer, 2019, pp. 395–406.
[9] Y. Li, K. Du, and J. Zhang, “Design of ring oscillator with temperature compensation effect,” Int. J. RF Microw. Comput.-Aided Eng., vol. 32, no. 11, Art. no. e23374, Nov. 2022.
[10] H. H. Hammam, K. M. Hassan, and S. A. Ibrahim, “An ultra-low-power process-and-temperature compensated ring oscillator,” in Proc. 9th Int. Conf. ICEEE, Alanya, Turkey, Mar. 2022.
[11] S. Zhang, A. Li, Y. Han, L. Jie, X. Han, and R. C. C. Cheung, “Temperature compensation technique for ring oscillators with tail current,” Electron. Lett., vol. 52, no. 13, pp. 1108–1110, Jun. 2016.
[12] M. Ortner and M. Punzenberger, “Systems and methods for oscillators using quadratic temperature compensation,” U.S. Patent 9 748 962 B2, Aug. 29, 2017.
[13] D. Patrinos and G. Souliotis, “A low-voltage, low-power 2.5 GHz ring oscillator with process and temperature compensation,” J. Low Power Electron. Appl., vol. 15, no. 3, Art. no. 52, Sep. 2025.
[14] M. Sivasakthi and P. Radhika, “Design and analysis of PVT tolerant hybrid current starved ring VCO with bulk driven keeper technique at 45 nm CMOS technology for the PLL application,” AEU – Int. J. Electron. Commun., vol. 173, Art. no. 154987, Jan. 2024.
[15] S. Madheswaran and R. Panneerselvam, “Design and analysis of 7-stage MOS current mode logic power gated MOSFETs in current starved VCO for the PLL application,” Int. J. Electr. Comput. Eng., vol. 14, no. 2, pp. 1398–1405, Apr. 2024.

## Slide 35
35
Thank You
Project-I (2026) · SENSE · VIT Chennai · github.com/pocopepe/visualizer