## Slide 1
1
School of Electronics Engineering (SENSE)
Project-I (2026)
Design of a Temperature-Compensated PLL Frequency Synthesiser
Student Name(s):
Aaryan Dogra (23BEC1032) · Yugeshwaran (23BEC1404) · Viju Sanjai (23BEC1306)
Guide:
Dr. B. Bindu, School of Electronics Engineering (SENSE)
Programme / School:
B.Tech — SENSE, VIT Chennai
Review & Date:
Review-II · 30.09.2026 (Wednesday)
Guide's Signature with Date
Signature: _____________________
Date: _________________________

## Slide 2
2
Introduction & Problem Recap
Problem recap
A PLL's ring-VCO drifts with temperature -- threshold voltage, mobility and capacitance all shift, so the same control voltage gives a different frequency hot vs. cold.
A compensation network cancels this by design, but sizing it needs a drift figure measured on the real topology, in the real process -- not assumed.
Objectives
Design an integer-N charge-pump PLL (ref -> PFD -> charge pump -> loop filter -> 5-stage current-starved ring VCO -> /8 divider) in sky130, open-source, headless.
Measure uncompensated drift across all 5 process corners, then design and validate a temperature-compensation network with real statistical rigor (Monte Carlo + hypothesis testing).
Refinements after Review-I feedback
Full 5-corner grid run (tt/ff/ss/sf/fs), not a 3-corner spot-check -- corrected the reported tempco spread from 3.4x to the real 12.5x (112-1399 ppm/C).
Cold-start acquisition risk (flagged as open in Review 1) fixed and verified: a true 0V cold start now locks in 839 ns.
Added a second-order (curvature-matched) compensation network, novelty-checked against prior art before committing to the claim (see Literature Review).

## Slide 3
3
Detailed Literature Review
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
1 | G. Souliotis et al., 2022 | Temperature compensated ring oscillator based VCO, AEU Int. J. Electron. Commun. | PTAT current compensation of a ring VCO inside a PLL; 180nm, 480MHz, fabricated | Closest topology benchmark: -1.5%/+0.4% over -40->120C, measured. First-order only; different node
2 | C. Stancu et al., 2023 | Temp. and power-supply compensated CMOS clock circuit based on ring osc., Electronics | Temp + supply compensated 50MHz ring-oscillator clock; simulation only | 1.6% temperature error pre-layout. A clock circuit, never closed into a PLL
3 | Z. Geng et al., 2018 | Low power fast locking PLL freq. synthesizer with temp. compensation, EAME | Freq. presetting + dynamic loop BW + static/dynamic temp. comp.; 180nm, 2.1-2.6GHz | Lock <2us over 0-80C, -117dBc/Hz@1MHz, 9mW. Stability claim is the locked output, set by the crystal
4 | Y. You et al., 2014 | 12GHz 67% tuning, 0.37ps RJrms PLL, LC-VCO temp. comp., 0.13um CMOS, IEEE RFIC | LC-VCO PLL for serial links; comp. scheme preserves tuning range; 5.6-13.4GHz | Stays locked -40->85C. Needs inductor models our process supports poorly; not portable to a ring VCO
5 | S. Sinha, 2002 | Design of an integrated CMOS PLL frequency synthesizer, IEEE MELECON | Dual-loop CP-PLL, 0.35um, 2.4-2.5GHz, 1MHz steps | -82dBc/Hz@10kHz. Architectural reference for our loop; no temperature compensation
6 | E. M. V. Freitas et al., 2025 | Using open source EDA tools in ASICs for HEP: a mixed comparison, JINST | Open-source vs commercial flows on IHP 130nm blocks incl. a current-starved ring VCO | Digital QoR quantified (+53% area, +118% power); analog VCO comparison qualitative, open-loop, no MC
7 | M. Thiriloganathan et al., 2026 | 2.4GHz LC-VCO fractional-N PLL, open-source, 130nm BiCMOS, SMACD | Fully open-source flow (Xschem/ngspice/KLayout/OpenEMS), EM-modelled inductor | -100.8dBc/Hz@1MHz. Closes a loop open-source, but no temp. compensation, no PVT/Monte Carlo
8 | R. N. S. Raphael et al., 2019 | PLL-based frequency synthesizer for digital systems driving, BTSym'18 (Springer) | 3rd-order CP-PLL for clock generation, integer-N (N=8-16), VCO input-cap-aware LF model | Settling <2us. Same loop class as ours; no temperature compensation

## Slide 4
4
Detailed Literature Review (contd.)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
9 | Y. Li, K. Du, J. Zhang, 2022 | Design of ring oscillator with temperature compensation effect, Int. J. RF Microw. CAE | Positive-TC supply voltage on a 31-stage ring, 0.18um; 33kHz sleep timer | 120 ppm/C (1.6%) over -40->80C. Single linear coefficient; kHz timer, not a PLL
10 | H. H. Hammam et al., 2022 | An ultra-low-power process-and-temperature compensated ring oscillator, IEEE ICEEE | 3-stage current-starved ring, 130nm, process + temperature compensation | Up to 90% less variation vs. plain current-starved ring, 346nW. Standalone oscillator
11 | S. Zhang et al., 2016 | Temperature compensation technique for ring oscillators with tail current, Electron. Lett. | Tail current = constant source + PTAT current, first-order | Foundational first-order technique; no numbers reported in abstract; not closed-loop
12 | M. Ortner, M. Punzenberger, 2017 | Oscillators using quadratic temperature compensation, US Pat. 9,748,962 B2 | Linear + quadratic temperature term for a VCO, -40->85C | Generic 2nd-order compensation is patented -- narrows our claim to ring-VCO + closed PLL + open PDK + stats
13 | D. Patrinos, G. Souliotis, 2025 | Low-voltage, low-power 2.5GHz ring oscillator with process & temp. comp., JLPEA | PTAT current + process-corner detection/tuning; 22nm, 0.8V; post-layout sim | Drift 23.9%->5.4% (tt) and 47.3%->7.2% (PVT). Corner-aware like our C(corner); not in a PLL
14 | M. Sivasakthi, P. Radhika, 2024 | PVT tolerant hybrid current starved ring VCO, bulk-driven keeper, 45nm, AEU | Two current-starved ring VCOs; Cadence GPDK45; corner + Monte Carlo | 6.97GHz, -121.5dBc/Hz@1MHz. PVT tolerance of the VCO itself, no compensation network or loop
15 | S. Madheswaran, R. Panneerselvam, 2024 | 7-stage MCML power-gated current starved VCO for PLL, IJECE | MOS current-mode logic delay cells with power gating, 45nm, simulation | 3.06GHz, -125.9dBc/Hz. Same device class as ours; no closed-loop temperature characterisation
Research gap (from all 15): no reported work combines a compensated ring VCO inside a closed loop, characterised across process corners with Monte Carlo rigor -- that gap is what this project fills.

## Slide 5
5
System Design & Architecture
Integer-N charge-pump PLL: REF -> PFD -> charge pump -> passive loop filter -> 5-stage current-starved ring VCO -> /8 divider, with a compensation network on the VCO bias path.
Scoping decisions (deliberate, documented): charge pump is an idealised 20uA behavioural source (transistor-level is Review 3, once layout needs real devices anyway).
PFD uses edge-detectors + NOR SR-latches, not resettable DFFs -- a reliable async reset fights the latch's own bistable feedback loop.
Notes: Insert your architecture / block diagram here.

## Slide 6
6
Implementation Details
Modules developed and integrated
VCO (5-stage current-starved ring), PFD, charge pump, passive loop filter, /8 divider, digital primitive cell library (INV/TG/DFF/TFF) -- all hand-written SPICE, ngspice, headless.
Temperature-compensation network: 1st-order (PTAT/CTAT-equivalent) and empirically-refined 2nd-order (curvature-matched), as a parameterised behavioural correction voltage.
Acquisition-boosted charge pump (5x current until the divider's first edge) -- closes the cold-start dead-zone risk carried from Review 1.
Algorithms implemented
Coefficient derivation: analytical 1st-order (from the measured f(T) polynomial fit and K_VCO), then empirical 2nd-order refit against the measured post-1st-order residual -- zero extra simulation for the refinement step.
Statistics: paired t-test, Wilcoxon signed-rank (normal approximation), OLS regression with slope confidence interval -- hand-implemented (no scipy in this environment), self-tested.
Code snippet -- the compensation correction (ngspice behavioural voltage source)
Bcomp vctrl vctrl_nom V = 'k1*(T-27) + k2*(T-27)*(T-27)' ; k1 = -1.322e-4 V/C, k2 = 2.891e-7 V/C^2 (tt, empirically refined) ; verified via an isolated 4-line polarity test before use in the full loop

## Slide 7
7
Results & Analysis (75%)
VCO tuning: K_VCO ~= 669 MHz/V at 0.9V (polynomial fit, not a secant); 18->358 MHz over 0.65->1.40V. Oscillation lost below ~0.60-0.65V (device-threshold-limited).
Full 5-corner grid (all of tt/ff/ss/sf/fs, not a 3-corner spot-check) -- corrects the Review-1 finding: real tempco spread is 12.5x, not 3.4x. Worst corner (fs) wasn't checked before.
Corner | NMOS/PMOS | K_VCO (MHz/V) | Uncompensated tempco
sf | slow / fast | 580.2 | +112 ppm/C (flattest)
ff | fast / fast | 763.6 | +332 ppm/C
tt | typical / typical | 669.3 | +681 ppm/C
ss | slow / slow | 568.2 | +1070 ppm/C
fs | fast / slow | 688.7 | +1399 ppm/C (steepest)
12.5x
spread, not the 3.4x previously reported
669
MHz/V K_VCO (tt, 0.9V, fit-derivative)
Sensitivity insight: N/P-mismatched corners (sf, fs) bracket the entire tempco range, not the matched-speed corners (ff, ss) -- points at current-source balance, not absolute device speed, as the driving mechanism.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 8
8
Results & Analysis (contd.)
Compensation refit independently at every corner; every corner improves at both stages. Checked at 4 held-out temperatures never used in fitting (-30/10/40/70C): all stay inside the fitted envelope.
Corner | Baseline span | 1st-order span | 2nd-order span | 2nd-order max ¦dev¦ | Meets +/-0.3%?
ff | 4.15% | 1.06% | 0.10% | 0.07% | Yes
sf | 1.40% | 0.42% | 0.24% | 0.15% | Yes
tt | 8.51% | 3.05% | 1.12% | 0.87% | No
ss | 13.37% | 6.37% | 3.32% | 2.46% | No
fs | 17.49% | 9.13% | 5.31% | 3.83% | No
Our +/-0.3% target is met at ff and sf only -- not at the typical corner. Closing the gap needs a transistor-level network whose PTAT slope tracks process, and/or a per-corner trim (Review 3).
Naive analytical 2nd-order coefficients made tt worse (4.49% vs 3.05%): they assume constant K_VCO, which is false. Refitting against the measured 1st-order residual fixed it.
Scope: compensation is an ideal behavioural correction voltage (transistor-level in Review 3); closed-loop results are tt / 27 °C.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 9
9
Results & Analysis (contd.) -- Closed-Loop Lock
Quantity | Coarse-tuned start (0.85V) | TRUE cold start (0V, boosted)
Lock time | 577 ns | 839 ns
Settled V_ctrl | 0.902 V | 0.9002 V
Settled f_VCO | 227.96 MHz | 226.42 MHz
Spec / prediction | < 2us spec; ~450ns analytical | < 2us spec
Cold-start acquisition dead zone (open risk since Review 1) -- fixed and verified. Built a 5x-boosted-current charge pump variant that reverts to nominal current once the divider produces its first edge (tracked via a B-source-charged integrating capacitor, reusing the same current-injection idiom already proven correct -- not a new digital latch and its metastable-initial-state risk).
Simulated from a TRUE 0V cold start (not the coarse-tuned 0.85V assumption): locks in 839 ns, comfortably inside the 2us spec -- worked on the first simulation attempt.
Two real bugs found and fixed while closing the original loop (Review 1): an inverted SPICE B-source node-order convention (caught with a 5-line isolated test before touching the full loop), and an inconsistent loop-filter capacitor initial condition (a 50ns charge-pump hold gate was added to test a wrong hypothesis first -- disproving it is what pointed at the real cause).
Scope: compensation is an ideal behavioural correction voltage (transistor-level in Review 3); closed-loop results are tt / 27 °C.

## Slide 10
10
Results (contd.) -- Monte Carlo & Benchmark
Arm (tt, mismatch on, paired by seed) | n | Mean ¦drift¦, 85C vs -40C | 95% CI
Baseline (uncompensated) | 12 | 18.93 MHz (8.4%) | [16.20, 21.65]
1st-order | 30 | 5.86 MHz (2.6%) | [4.62, 7.09]
2nd-order (curvature-matched) | 30 | 3.37 MHz (1.5%) | [2.33, 4.41]
Both stages significantly reduce drift (12/12 seeds). 2nd-order beats 1st-order: -2.48 MHz, 95% CI [0.81, 4.15], paired t-test and Wilcoxon agree, 23/30 seeds.
Correction on record: our first pass tested signed drift and overstated this at n=12 (1st-order over-corrects, so the sign flipped). On |drift| it was not significant at n=12 -- n=30 is what earns the claim.
Design | Process | Residual drift | Lock time
This work, 2nd-order (tt) | sky130, simulation | +/-0.87% max dev., -40 to 85C | 839 ns (0V cold start)
Souliotis et al. 2022 [1] | 180nm, measured silicon | -1.5% / +0.4%, -40 to 120C | not reported
Stancu et al. 2023 [2] | simulation, 50 MHz clock | 1.6% temperature error | n/a
Geng et al. 2018 [3] | 180nm, measured silicon | not reported as drift | < 2 us
Comparable to published work, but ours is simulation of an ideal correction network vs. their measured silicon -- not a like-for-like claim until the transistor-level network exists.
Scope: compensation is an ideal behavioural correction voltage (transistor-level in Review 3); closed-loop results are tt / 27 °C.

## Slide 11
11
Challenges & Remaining Work
Challenges faced and solutions
SPICE B-source polarity and an inconsistent loop-filter initial condition broke the first closed-loop runs -- each isolated with a minimal test (and one wrong hypothesis disproved) before touching the full loop.
Naive analytical 2nd-order coefficients over-corrected the cold end -- fixed by refitting against the measured 1st-order residual; the refit was then checked at 4 held-out temperatures it never saw.
Caught our own statistics error: the first Monte Carlo pass compared SIGNED drift, which made 1st- vs 2nd-order look significant only because the sign flipped. Re-tested on |drift| and re-run at n=30.
Novelty check found a 2017 patent on generic quadratic compensation -- narrowed our claim to ring-VCO + closed-loop PLL + open PDK + statistically validated quantification.
Remaining work (25%)
Close the spec gap: +/-0.3% is met at ff and sf only (tt 0.87%, ss 2.46%, fs 3.83%) -- a transistor-level compensation network whose PTAT slope tracks process, plus a per-corner trim.
Transistor-level charge pump; layout in Magic, DRC, LVS (netgen), post-layout re-simulation.
Cadence/Virtuoso cross-validation arm and the actual H1 regression (eps_res vs C) -- the other half of the research hypothesis, pending lab access.
Timeline to Review-III (28.10.2026)
Weeks 1-2: transistor-level CP + compensation network. Week 3: layout / DRC / LVS. Week 4: Virtuoso arm, H1 regression, final report.

## Slide 12
12
References
[1] G. Souliotis, E. Keramida, F. Plessas, R. Malatesta, and S. Vlassis, “Temperature compensated ring oscillator based VCO,” AEU – Int. J. Electron. Commun., vol. 149, Art. no. 154195, May 2022.
[2] C. Stancu, A. Neacsu, O. Profirescu, D. Dobrescu, and L. Dobrescu, “Temperature and power supply compensated CMOS clock circuit based on ring oscillator,” Electronics, vol. 12, no. 3, Art. no. 507, Jan. 2023.
[3] Z. Geng, X. Ma, and Z. Li, “A low power fast locking PLL frequency synthesizer with temperature compensation,” in Proc. 3rd Int. Conf. EAME, Atlantis Press, Jun. 2018, pp. 281–285.
[4] Y. You, D. Huang, J. Chen, and S. Chakraborty, “A 12GHz 67% tuning range 0.37ps RJrms PLL with LC-VCO temperature compensation scheme in 0.13µm CMOS,” in Proc. IEEE RFIC, Tampa, FL, USA, Jun. 2014, pp. 101–104.
[5] S. Sinha, “Design of an integrated CMOS PLL frequency synthesizer,” in Proc. 11th IEEE MELECON, Cairo, Egypt, 2002, pp. 220–224.
[6] É. M. V. Freitas et al., “Using open source EDA tools in ASICs for HEP: A mixed comparison,” J. Instrum., vol. 20, no. 12, Art. no. P12022, Dec. 2025.
[7] M. Thiriloganathan et al., “A 2.4 GHz LC-VCO fractional-N phase locked loop open-source design in 130-nm BiCMOS,” in Proc. 22nd Int. Conf. SMACD, 2026, arXiv:2607.08852.
[8] R. N. S. Raphael, A. M. Pinto, L. T. Manera, and S. Finco, “Phase-locked loop (PLL)-based frequency synthesizer for digital systems driving,” in Proc. BTSym’18, SIST vol. 140, Springer, 2019, pp. 395–406.
[9] Y. Li, K. Du, and J. Zhang, “Design of ring oscillator with temperature compensation effect,” Int. J. RF Microw. Comput.-Aided Eng., vol. 32, no. 11, Art. no. e23374, Nov. 2022.
[10] H. H. Hammam, K. M. Hassan, and S. A. Ibrahim, “An ultra-low-power process-and-temperature compensated ring oscillator,” in Proc. 9th Int. Conf. ICEEE, Alanya, Turkey, Mar. 2022.
[11] S. Zhang, A. Li, Y. Han, L. Jie, X. Han, and R. C. C. Cheung, “Temperature compensation technique for ring oscillators with tail current,” Electron. Lett., vol. 52, no. 13, pp. 1108–1110, Jun. 2016.
[12] M. Ortner and M. Punzenberger, “Systems and methods for oscillators using quadratic temperature compensation,” U.S. Patent 9 748 962 B2, Aug. 29, 2017.
[13] D. Patrinos and G. Souliotis, “A low-voltage, low-power 2.5 GHz ring oscillator with process and temperature compensation,” J. Low Power Electron. Appl., vol. 15, no. 3, Art. no. 52, Sep. 2025.
[14] M. Sivasakthi and P. Radhika, “Design and analysis of PVT tolerant hybrid current starved ring VCO with bulk driven keeper technique at 45 nm CMOS technology for the PLL application,” AEU – Int. J. Electron. Commun., vol. 173, Art. no. 154987, Jan. 2024.
[15] S. Madheswaran and R. Panneerselvam, “Design and analysis of 7-stage MOS current mode logic power gated MOSFETs in current starved VCO for the PLL application,” Int. J. Electr. Comput. Eng., vol. 14, no. 2, pp. 1398–1405, Apr. 2024.

## Slide 13
13
Thank You
Project-I (2026) · SENSE · VIT Chennai · github.com/pocopepe/visualizer